## Slide 1
Integrated Smart Traffic System
Prepared By:
Khawla Al-Shaikh
Judy Dukmak
Supervised By:
Dr.Riad Sonbol
Eng.Aya Alaswad

## Slide 2
Introduction,Objective & project signification
Agenda
Research Paper Comparison
Datasets Comparison & Overview
Project Pipeline
Arguments
2
1
3
4
5

## Slide 3
A smart control signal is an advanced traffic management system that uses sensors, cameras, and real-time data to control traffic lights automatically. It helps regulate the flow of vehicles based on current road conditions instead of fixed timing. With increasing urban traffic, traditional traffic lights often cause congestion and delays. Smart control signals aim to improve road efficiency, safety, and overall transportation management.
The objective of a smart control signal system is to improve traffic flow by adjusting signal timings according to real-time traffic conditions. It aims to reduce traffic congestion and waiting time at intersections. Another goal is to enhance road safety for drivers, cyclists, and pedestrians. The system also seeks to make transportation more efficient through the use of modern technology.
Objective
The significance of smart control signals lies in their ability to reduce traffic congestion and save travel time for road users. They help lower fuel consumption and reduce air pollution caused by vehicles waiting at intersections. Smart signals also contribute to safer roads by managing traffic more effectively. Additionally, they support the development of smarter and more sustainable cities.
Significance of the Study
Introduction

## Slide 4
Full Title | Adaptive Neural Traffic Orchestration: AI-Driven Network Optimization for Dynamic Congestion Mitigation(2020) | Adaptive urban traffic signal control based on enhanced deep reinforcement learning(2024) | Joint Pedestrian and Vehicle Traffic Optimization in Urban Environments using Reinforcement Learning(2025)
Base Model | Hybrid deep learning and reinforcement learning framework combining Graph Convolutional Networks (GCN) for spatial traffic modeling, LSTM-based temporal prediction, and Proximal Policy Optimization (PPO) for multi-objective traffic control decision making. | DRL based on Deep Q-Network (DQN) with Value-based architecture, enhanced into a Dueling Double Deep Q-Network (D3QN), and further extended into the proposed PN_D3QN model by integrating prioritized experience replay (PER) and noisy network mechanisms. | Deep Reinforcement Learning framework for corridor-level Adaptive Traffic Signal Control (ATSC) using Proximal Policy Optimization (PPO) with Actor–Critic architecture.
Training Approach | Policy learning is performed using the Proximal Policy Optimization (PPO) algorithm within a reinforcement learning framework where the agent interacts with a simulated urban traffic environment. reinforcement agent optimized with multi-objective rewards balancing travel time, emissions, fairness, and stability. | The agent is trained to approximate the optimal action-value function using a convolutional and fully connected neural network. Transitions are stored as (s, a, r, s′) in replay memory. The model integrates dueling network architecture, double Q-learning, and noise injection, with parameters updated through gradient descent to maximize expected reward. | Centralized training Single Agent trained using (PPO) with Generalized Advantage Estimation (GAE), Training occurs across 24 parallel actors over 6 × 10⁶ simulation timesteps.
Results Summary | Compared to fixed-time control, ANTO achieved a 27% reduction in average travel time, 36% drop in congestion delays, ~23% lower emissions, and improved throughput and fairness. | The enhanced DRL model converged faster than baseline DRL, and demonstrated lower average waiting times and queue lengths, showing robustness across various traffic densities. | Average pedestrian and vehicle wait times reduced (~67% and ~52% respectively) compared to fixed signals; generalization capabilities across varying traffic demands.
Research Paper Comparison
DRL papers:

## Slide 5
Limitations / Research Gaps | Relies on high-quality real-time data; not fully tested under extreme events or sensor failures; computational demands may be high. current implementation does not fully account for emerging mobility services like ride-sharing and autonomous vehicles. | The study is limited to a single intersection scenario. No real-world deployment. The framework does not extend to multi-agent or network-level signal coordination. More real-world traffic data is suggested for future validation. The cold-start problem remains unresolved during early training. | 1-vehicle queue propagation upstream when signals are closely spaced 2- high switching frequency, increase vehicle energy consumption 3- evaluation was limited to a university campus setting 4- baselines include common real-world approaches direct comparison with other RL-based controllers proved challenging, No mixed-traffic (AV + human) modeling.
state representation | The state represents the current traffic conditions across the network. | The state is encoded using discrete matrix representations of vehicle positions and velocities, along with the current signal phase. Each lane is divided into grids to capture spatial vehicle distribution, forming position and velocity matrices that represent real-time traffic conditions at the intersection. | Spatio-temporal stacked occupancy representation. previous phase (N=10 steps)
action selection | Actions are selected by the PPO policy network, which generates a vector of control decisions, including signal timing adjustments, recommended route changes, and demand management strategies. | The agent selects the green light duration for the current signal phase based on the maximum Q-value output from the neural network. Action selection follows a phase-cycled structure. | two components: Intersection Action: Four predefined phase configurations, selection is drawn from a Categorical distribution; Mid-block Actions: For each of 7 signals, selects a binary action each modeled as a Bernoulli distribution.
Action Scope | Network-wide control decisions including signal timing adjustments, route guidance recommendations, and demand management strategies designed to redistribute traffic demand and mitigate congestion. | The model adjusts only the green light duration of the current phase within a fixed cyclic phase sequence. The action set consists of predefined green durations. Single intersection | 8 signals: 1 main intersection+ 7 mid-block signals

## Slide 6
https://1drv.ms/w/c/0d77e4f105f88a3b/IQBuJSzVrNyFTZA8z3ALJ7I8AfyqfPK9ESLQw68dut1-XU0?e=5YPKvE
Agent Type | Centralized single-agent reinforcement learning controller managing network-wide traffic operations. | Single-agent reinforcement learning controller managing traffic signal timing at a single intersection, where one centralized agent observes the intersection traffic state and selects the optimal signal phase duration using a Deep Q-Network–based policy. | Single-agent reinforcement learning controller optimizing traffic signal timing for both pedestrian crossings and vehicle movements along an urban corridor, where a centralized agent makes phase control decisions based on combined pedestrian and vehicle traffic states.
reward design | Multi-objective (travel time, emissions, fairness, stability) | difference in total queue length between consecutive action time step | Exponentially Increasing Maximum Wait Aggregated Queue (EI-MWAQ); L2 aggregation + exponential penalty
DRL Structure | The decision optimization module follows an Actor–Critic architecture using the PPO algorithm, where a policy network generates traffic control actions, and a value network estimates the value of network traffic states. The framework operates on graph-structured traffic data and integrates predictive traffic features generated by the GCRNN model. | The framework is based on an enhanced DQN architecture combining convolutional layers for traffic feature extraction and fully connected layers for Q-value estimation. It adopts dueling network decomposition, double Q-learning with main and target networks, prioritized experience replay, and noisy network parameters to improve convergence speed, stability, and robustness. | Algorithm: PPO Actor–Critic Architecture Separate MLP networks Hidden layers (Actor): [512, 256, 128, 64, 32] Hidden layers (Critic): [512, 256, 128, 64, 32]
Evaluation Metrics | Average travel time , Total Traffic Delay, Throughput , CO₂ Emissions , Fairness Index (Jain's fairness index) , System Responsiveness to Incident events. | Cumulative Reward per episode Average Waiting Time per lane (seconds) Average Queue Length per lane (vehicles) . | Avg & total wait time (vehicle & pedestrian), conflict count, phase switching frequency, generalization under unseen demand.
Details:

## Slide 7
Datasets Comparison Table
Table 1: General Dataset Characteristics
Dataset | Data Type | Size | What it Contains | Annotations
Performance Measurement System (PeMs) | Real highway sensor data | thousands of highway sensors across California; multi-year measurements | traffic flow, speed, occupancy, timestamps | sensor metadata including location and lane
Manchester Traffic Dataset | Real-world traffic counts dataset | includes 338 count points, 37,572 raw traffic records, 4,631 daily flow records, and 8,419 directional flow records | vehicle counts at road count points, traffic by vehicle class, annual average daily flow, directional traffic flow | metadata including count location, estimation method, road type
SUMO Traffic Scenarios (Toronto, Monaco, Cologne, etc.) | Simulation dataset | range from single intersection, corridors, district-level networks, to full city simulations | road network topology, intersections, lanes, vehicle routes, traffic signals | vehicles and routes defined explicitly in simulation files
Hangzhou Traffic Signal Control Dataset | Real traffic data converted to simulation | 1 intersection (1×1) to 16 intersections (4×4 grid); simulation duration 3600 s | road network and traffic flows derived from camera data | turning ratios estimated (10% left, 60% straight, 30% right) due to missing turn records
Traffic Flow Dataset - Zenodo | real-world networks + simulated traffic demand for SUMO | 10 networks (6 synthetic + 4 real), 22 optimization instances, each with 1200 traffic demand inputs | traffic volume inputs, generated vehicle routes, SUMO network definitions | traffic demand definitions per network
Notes: 7

## Slide 8
Table 2: Inputs, Outputs, and Use cases
Dataset | Inputs | Outputs | Use Cases
Performance Measurement System (PeMs) | sensor measurements at time intervals (e.g., 5-min aggregation) | predicted traffic speed or flow in forecasting tasks | traffic flow prediction, congestion analysis, spatio-temporal modelling
Manchester Traffic Dataset | traffic counts from manual and automatic roadside sensors | traffic volume statistics such as vehicles per day | traffic demand analysis, urban traffic statistics, traffic forecasting
SUMO Traffic Scenarios | network file (.net.xml), route file (.rou.xml), configuration (.sumocfg) | vehicle travel time, delay, queue length, throughput | traffic signal optimization , traffic simulation experiments, RL training
Hangzhou Traffic Signal Control Dataset | roadnet.json, flow.json | average travel time used for evaluation | reinforcement learning traffic signal control benchmarks
Traffic Flow Dataset - Zenodo | traffic volume inputs τ used by JTRrouter to generate routes | vehicle routes and traffic simulation outputs | traffic signal timing optimization research
For more details: https://1drv.ms/w/c/c8c8909e9d56f63b/IQALlcaaL1XaTrWo7oRUT6KBAdZJfm0uo1k9sgraPBjeTrE?e=Q8kpz3

## Slide 9
For more details:
https://1drv.ms/w/c/0d77e4f105f88a3b/IQDaD9_1304MQ7Xpa1FvlGjJATZq1T-t3sWBVBmC2fOWpr4?e=MmeTBW
(hangzhou_1x1_kn-hz_18041608_1h)
represents traffic data from a single intersection (1×1 road network) in Hangzhou, China.
The dataset covers one hour (3600 seconds) of traffic collected on April 16, 2018.
It is designed for experiments using the CityFlow traffic simulator to study traffic signal control strategies.
The input of the dataset includes the road network structure (roadnet.json) and vehicle flow information (flow.json), which describe lane connections, signal phases, vehicle routes, and arrival times.
These files define how vehicles move through the intersection during the simulation.
The traffic volume in this dataset is relatively light, making it suitable for analyzing traffic control under lower demand conditions.
The output of simulations using this dataset includes: vehicle travel time, waiting time, queue length, and traffic signal performance metrics. These outputs help evaluate how efficiently a traffic signal control algorithm manages the intersection.
Dataset Overview

## Slide 10
Project Pipeline
Stage 1: Understand Hangzhou Dataset Structure
│
▼
Stage 2: Parse JSON Files │
▼
Stage 3: Build Traffic Simulation Environment
Stage 4: Design State Representation
│
▼
Stage 5: Define Action and Reward Structure
│
▼
Stage 6: Implement PPO Agent
Stage 7: Train Agent on Simulation
│
▼
Stage 8: Hyperparameter Tuning
│
▼
Stage 9: Evaluate Performance
│
▼
Stage 10: Analyze and Document Results
│
▼
Reward Calculation
│
▼
Policy Update (Training)
└──── repeat
1
2
3

## Slide 11
We are pleased to hear your questions!
if you have any question don’t keep it in your mind!
Arguments
Thank You
Why This Project?
Urban traffic congestion is a major challenge in modern cities.
Traditional traffic lights use fixed timing plans that cannot adapt to real-time traffic conditions and dynamic environments.
Recent research shows that Reinforcement Learning can significantly improve traffic signal control by learning adaptive policies based on real traffic states.
Expected Contributions
This project aims to:
Implement an adaptive traffic signal control system using Deep Reinforcement Learning.
Evaluate the effectiveness of RL compared to fixed-time signal control.
Demonstrate the feasibility of intelligent traffic management for smart city applications.
Future Extension
The system can later be extended to:
Multi-intersection traffic control
Integration with smart city traffic management systems
Enable cooperation with other intelligent agents such as:
Parking assistant agent for guiding vehicles to available parking spaces.
Incident detection agent for handling accidents.